## Slide 1: HTTP/2.0 Servlet 4.0

## Slide 2
HOW WE GOT HERE
1991
HTTP 0.9
1996
HTTP 1.0
2009
SPDY 1.0
1999
HTTP 1.1
2015
HTTP 2.0

## Slide 3
HTTP/2.0 based on SPDY ( developed by GOOGLE )
TESTS OF SPDY SHOWED :
in some cases, pages were loaded 55% faster
the average load time was reduced by 36%
HTTP HISTORY
SPDY
protocol

## Slide 4
Browser Compatibility of HTTP/2

## Slide 5
22.3% of all Web sites support the HTTP/2 protocol
SUPPORT OF HTTP/2

## Slide 6
SUPPORT OF HTTP/2
IIS: Windows Server 2016
Apache 2.4.17
nginx 1.9.5
Apache Tomcat 9.0.0.M17
WildFly 10 (Undertow)
Jetty Stable-9
Netty 4.1
Payara 5.0
Vert.x
GlassFish 5.0

## Slide 7
Total Transfer Size & Total Requests

## Slide 8
Problem of HTTP/1.1
Responds in sequence
Head-of-Line blocking
One request per TCP connection
HTTP header fields are often repetitive and verbose

## Slide 11
Web request-response lifecycle
(Worst case) DNS lookup to resolve the hostname to IP address
(Worst case) New TCP connection, requiring a full roundtrip to the server
(Worst case) TLS handshake with up to two extra server roundtrips!
HTTP request, requiring a full roundtrip to the server
Server processing time
DNS LOOKUP
HTTP REQUEST
SOCKET CONNECT
CONTENT DOWNLOAD

## Slide 12
How developers resolves problems of HTTP 1.1
Creating sprites
Inlining
Joining
Sharing

## Slide 13
How HTTP/2.0 resolves problems
Request/Response multiplexing
Stream Prioritization and Dependency
Server Push
Header compression

## Slide 14
HTTP/2.0 key concepts
• Connection – single TCP connection
• Streams - channel that carries messages in two directions
• Messages - request or response
• Frames – messages, which are broken down for sending

## Slide 15
HTTP/2 Units
CONNECTION
STREAM
FRAME
FRAME
FRAME
FRAME
FRAMEs have:
flags
type
stream id
length
payload
STREAMs have:
identifier
state
priority
flow control
CONNECTION have:
flow control

## Slide 16
Binary Framing
STREAM IDENTIFIER (31)
FRAME PAYLOADS (0..N)
LENGTH (24)
R
TYPE (8)
FLAGS (8)

## Slide 17
Type of Frames in HTTP/2.0
DATA
Used to transport HTTP message bodies
HEADERS
Used to communicate header fields for a stream
PRIORITY
Used to communicate sender-advised priority of a stream
RST_STREAM
Used to signal termination of a stream
SETTINGS
Used to communicate configuration parameters for the connection

## Slide 18
PUSH_PROMISE
Used to signal a promise to serve the referenced resource
PING
Used to measure the roundtrip time and perform "liveness" checks
GOAWAY
Used to inform the peer to stop creating streams for current connection
WINDOW_UPDATE
Used to implement flow stream and connection flow control
CONTINUATION
Used to continue a sequence of header block fragments
Type of Frames in HTTP/2.0

## Slide 19
HTTP/2.0 HEADLINE FEATURE
Multiplexing
Priority
Flow control
Header compression
Server push

## Slide 20
Multiplexing
Priority
Flow control
Header compression
Server push
HTTP/2.0 HEADLINE FEATURE

## Slide 21
Request/Response Multiplexing

## Slide 22
Maximum concurrent open TCP connections
Browser | Parallel connections per hostname
Chrome | 6
Firefox | 6
Opera | 6
Safari | 6
Internet Explorer 11 | 13
Microsoft Edge | 13

## Slide 23
Request/Response Multiplexing

## Slide 24
HTTP 1.1 round-trip
Host: maven.apache.org
SecurityToken: j13c72208c9u5fa2
Accept: application/json
Accept-Encoding: gzip
GET /install.html HTTP/1.1
Content-Length: 327
Cache-Control: private, max-age=60, s-maxage=0
Vary: SecurityToken
Date: Wed, 17 Jan 2018 21:31:57 GMT
Content-Type: application/json
Content-Encoding: gzip
GET /install HTTP/1.1
GZIPPED DATA

## Slide 25
HTTP/2 round-trip
:method: GET
:authority: maven.apache.org
:path: /install.html
securitytoken: j13c72208c9u5fa2
accept: application/json
accept-Encoding: gzip
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
:status: 200
content-Length: 327
cache-Control: private, max-age=60, s-maxage=0
vary: SecurityToken
date: Wed, 17 Jan 2018 21:31:57 GMT
content-Type: application/json
content-Encoding: gzip
HEADERS
Stream: 3
Flags: END_HEADERS
GZIPPED DATA
DATA
Stream: 3
Flags: END_STREAM

## Slide 26
Comparison requests of HTTP 1.1 & HTTP/2
:method: GET
:authority: maven.apache.org
:path: /install.html
securitytoken: j13c72208c9u5fa2
accept: application/json
accept-Encoding: gzip
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
Host: maven.apache.org
SecurityToken: j13c72208c9u5fa2
Accept: application/json
Accept-Encoding: gzip
GET /install.html HTTP/1.1

## Slide 27
Comparison responses of HTTP 1.1 & HTTP/2
:status: 200
content-Length: 327
cache-Control: private, max-age=60, s-maxage=0
vary: SecurityToken
date: Wed, 17 Jan 2018 21:31:57 GMT
content-Type: application/json
content-Encoding: gzip
HEADERS
Stream: 3
Flags: END_HEADERS
GZIPPED DATA
DATA
Stream: 3
Flags: END_STREAM
Content-Length: 327
Cache-Control: private, max-age=60, s-maxage=0
Vary: SecurityToken
Date: Wed, 17 Jan 2018 21:31:57 GMT
Content-Type: application/json
Content-Encoding: gzip
GET /install HTTP/1.1
GZIPPED DATA

## Slide 28
HTTP/2 interleaving
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 5
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 3
Flags: END_HEADERS
DATA
Stream: 5
Flags:
HEADERS
Stream: 5
Flags: END_HEADERS
DATA
Stream: 3
Flags: END_STREAM
DATA
Stream: 5
Flags: END_STREAM

## Slide 29
HTTP/2 canceling a Stream
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 5
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 3
Flags: END_HEADERS
DATA
Stream: 5
Flags:
HEADERS
Stream: 5
Flags: END_HEADERS
DATA
Stream: 3
Flags: END_STREAM
RST_STREAM
Stream: 5
ErrorCode: CANCEL

## Slide 30
HTTP/2 control frames
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 5
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 3
Flags: END_HEADERS
DATA
Stream: 5
Flags:
HEADERS
Stream: 5
Flags: END_HEADERS
DATA
Stream: 3
Flags: END_STREAM
DATA
Stream: 5
Flags: END_STREAM
SETTINGS
Stream: 0
Flags:
SETTINGS
Stream: 0
Flags: ACK

## Slide 32
Multiplexing
Priority
Flow control
Header compression
Server push
HTTP/2.0 HEADLINE FEATURE

## Slide 33
Stream Prioritization
Before any application data can be sent, a new stream must be created and the appropriate metadata such as HTTP headers must be sent.
In addition to the common header, an optional 31-bit stream priority has been added.

## Slide 34
HTTP/2 priority
HEADERS
Stream: 3
Flags: END_HEADERS, END_STREAM
HEADERS
Stream: 5
Flags: END_HEADERS, END_STREAM
Priority: 0
HEADERS
Stream: 3
Flags: END_HEADERS
DATA
Stream: 5
Flags:
HEADERS
Stream: 5
Flags: END_HEADERS
DATA
Stream: 5
Flags: END_STREAM
DATA
Stream: 3
Flags: END_STREAM
Priority: stream is more (lower number) or less (higher number) important
data might be sent earlier

## Slide 35
Stream Prioritization

## Slide 36
Multiplexing
Priority
Flow control
Header compression
Server push
HTTP/2.0 HEADLINE FEATURE

## Slide 37
HTTP/2 flow control

## Slide 38
HTTP/2.0 HEADLINE FEATURE
Multiplexing
Priority
Flow control
Header compression
Server push

## Slide 39
HTTP 1.1 headers

## Slide 40
HTTP/2 header compression

## Slide 41
HTTP/2 reference tracking

## Slide 42
Header compression

## Slide 43
Static Header Table

## Slide 44
Header compression

## Slide 45
Header compression

## Slide 46
HTTP/2.0 HEADLINE FEATURE
Multiplexing
Priority
Flow control
Header compression
Server push

## Slide 47
HTTP/2 push promise

## Slide 48
Comparison of time to fetch HTTP resources

## Slide 49
Comparison of HTTP 1.1 and HTTP/2
HTTP/1.1 Page Load | HTTP/2 Page Load
Create six to eight connections. | Create a single connection
Request HTML page | Request HTML page
Receive HTML page | Receive HTML page
Decode HTML page | Decode HTML page
Request first six to eight files included in the HTML page, no priorities or dependencies. (Requests have uncompressed, plain-text headers.) | Request all files included in the HTML page, with priorities and dependencies. (Requests have compressed, binary headers.)
On each connection, wait for requested file to arrive | (Files returned, multiplexed on single connection, as ready.)
Request next file on now-open connection | -
Repeat 6-7 for each remaining file | -
Close six connections | Close single connection

## Slide 50
When you don’t know if it supports HTTP/2
GET / HTTP/1.1
Host: server.example.com
Connection: Upgrade, HTTP2-Settings
Upgrade: h2c
HTTP2-Settings: <base64url encoding of HTTP/2 SETTINGS payload>
● “h2c” means no TLS connection
● “h2” means TLS connection [TLS-ALPN]
● A server MUST NOT upgrade the connection to HTTP/2 if this header field is not present or if more than one is present.
● A server MUST NOT send this header field.
[ Response ]
HTTP/1.1 101 Switching Protocols
Connection: Upgrade
Upgrade: h2c
Implicit acknowledgement of HTTP2-Settings

## Slide 51
 | 41 req 172 kb | 66 req 215 kb | 130 req 427 kb | 230 req 2.0 mb | 330 req 4.2 mb | 430 req 5.4 mb
HTTP/2 | 332.37 | 415.33 | 774.13 | 1.26 | 1.83 | 2.31
HTTP 1.1 | 545.67 | 629.30 | 877.77 | 1.40 | 1.94 | 2.46
% | 64.18 | 51.52 | 13.39 | 11.61 | 5.73 | 6.52

## Slide 53
Configure Tomcat 9 for HTTP/2
Open the conf/server.xml file and make the following configuration changes.
<Connector port="8443" protocol="org.apache.coyote.http11.Http11NioProtocol"
maxThreads="150" SSLEnabled="true" scheme="https" secure="true"
sslImplementationName="org.apache.tomcat.util.net.jsse.JSSEImplementation"
keystoreFile=“/conf/tomcat-sslkey" keystorePass=“*******"
clientAuth="false" sslProtocol="TLS">
<UpgradeProtocol className="org.apache.coyote.http2.Http2Protocol"/>
</Connector>

## Slide 54
Servlet 4.0 dependency
<dependency>
<groupId>javax.servlet</groupId>
<artifactId>javax.servlet-api</artifactId>
<version>4.0.0</version>
<scope>provided</scope>
</dependency>

## Slide 55
Servlet 4.0 brings HTTP/2 to Java EE
The Servlet API is well positioned to enable HTTP/2 optimization and to allow frameworks to leverage server push.
Expose key features to the API:
Server Push
Stream Prioritization
Request/Response multiplexing
Upgrade from HTTP 1.1

## Slide 56
Add a new class Priority:
exclusive ( ) : Boolean
streamId ( ): Int
weight ( ): Int
Add methods to HttpServletRequest:
getPriority ( ): Priority
getStreamId ( ): Int
Add methods to HttpServletResponse:
getPriority ( ): Priority
setPriority (Priority p): Unit
getStreamId ( ): Int
Servlet 4.0 New Features

## Slide 57
Servlet 4.0 New Features
Add method to ServletContext:
setRequestCharacterEncoding ( )
setResponseCharacterEncoding ( )
setSessionTimeout (minutes: Int)
addJspFile (name: String, jspFile:String)
Add new XML elements in web.xml:
<request-character-encoding />
<response-character-encoding />
<default-context-path />
Add new classes GenericFilter, HttpFilter

## Slide 58
Typical Journey
setPath(“/style.css”)
push( )
setPath(“/jquery.js”)
push( )
style.css
jquery.js
GET /index.html
index.html
browser
servlet
PushBuilder
request.newPushBuilder( )

## Slide 59
Push Builder from HTTP Request
fun getHttpSample(req: HttpServletRequest, resp: HttpServletResponse): String { req.newPushBuilder()?.path("/res/css/style.css")?.push() req.newPushBuilder()?.path("/res/images/logo.png")?.push() req.newPushBuilder()?.path("/res/images/background.jpg")?.push()
HttpServletRequest
getPushBuilder( ): PushBuilder
…( )
I
PushBuilder
addHeader(String, String): PushBuilder
etag(String): PushBuilder
lastModified(String): PushBuilder
queryString(String): PushBuilder
sessionId(String): PushBuilder
path(String): PushBuilder
push( )
…( )
I

## Slide 60
Push Builder from HTTP Request
fun push1(req: HttpServletRequest, resp: HttpServletResponse) { val pushBuilder = req.newPushBuilder() pushBuilder?.apply { for (i in 1..250) { pushBuilder .path("res/images/space/space_$i.jpg") .addHeader("content-type", "image/jpg") .push() } }

## Slide 61
Filter and Server Push feature
@WebFilter(urlPatterns = ["/*"])
class PushFilter : Filter {
override fun doFilter(req: ServletRequest, resp: ServletResponse, chain: FilterChain) {
val httpRequest: HttpServletRequest = req as HttpServletRequest
val requestURI = httpRequest.requestURI
val pushBuilder = httpRequest?.newPushBuilder()
when (requestURI) {
"index.html" -> {
      pushBuilder?.path("/style.css")?.push()
      pushBuilder?.path("/logo.png")?.push()
}
else -> pushBuilder?.path("/nature.png")?.push()
}
chain.doFilter(req, resp)
}
}

## Slide 62
Conclusion: what we get with HTTP/2
• 1 socket for 100+ concurrent streams.
• Advanced features like:
        flow control
        cancellation
        cache push.
• Dramatically less header overhead.

## Slide 63
THANK YOU!

## Slide 64
HTTP/2 клиент
Oracle планирует выкатить новый HTTP-клиент для поддержки протоколов HTTP/2 и WebSocket. Они заменяют HttpURLConnection API на новый, более производительный.
Новый API будет представлен в пакете «java.net.http». Он поддерживает как синхронный, так и асинхронный режимы.
Новый API можно посмотреть на официальном сайте Oracle в разделе документаций.
Пример HTTP/2 Client:
jshell> import java.net.http.*
jshell> import static java.net.http.HttpRequest.*
jshell> import static java.net.http.HttpResponse.*
jshell> URI uri = new URI("http://rams4java.blogspot.co.uk/2016/05/java-news.html")
uri ==> http://rams4java.blogspot.co.uk/2016/05/java-news.html
jshell> HttpResponse response = HttpRequest.create(uri).body(noBody()).GET().response()
response ==> java.net.http.HttpResponseImpl@79efed2d
jshell> System.out.println("Response was " + response.body(asString()))